## Slide 1: “Alexa, Stop Spying on Me!”: Speech Privacy Protection Against Voice Assistants
Ke Sun, Chen Chen, and Xinyu Zhang
SenSys’20 Nov 16th, 2020
University of California, San Diego

## Slide 2: Motivation
Over 4.2 Billion Devices Provide Voice Assistant Access Today
Voice Assistant Usage Seen Growing To 8.4 Billion Devices in 2024

## Slide 3
Privacy Issues has become a key concern for Voice Assistant consumer.

## Slide 4: Motivation: Privacy Concern
Always-on Microphone can upload your private speech to a remote cloud!

## Slide 5: Can we force the Voice Assistant to record the legitimate commands only, rather than private speech?
Selectively Jamming

## Slide 6: Our Vision
MicShield is a companion device which prevents VAs from recording private speech without affecting the VAs’ normal functionalities  Selectively Jamming

## Slide 7: Threat Model
MicShield targets the scenario where adversaries use VA’s always-on microphones to eavesdrop on private speech.
Protection Goals: Under the premise of not breaking the VAs’ functionalities, MicShield aims to prevent the private speech from reaching the VAs.
Private Speech: voice signals that are not preceded by a wake word.

## Slide 8: Challenge 1
How to enable the selective jamming automatically?
Stop Jamming
Jamming
Jamming

## Slide 9: Selective Jamming: Phoneme-level
Basic idea: identify wake words from its early onset from phoneme-level
Observation: Even with the first 60 ms muted or jammed, the wake word can still activate the Echo Dot with 95% accuracy–the same as the case without mute/jamming.
Alexa
120 ms
Switch off jamming after identifying the first phoneme

## Slide 10: Jamming Control Pipeline

## Slide 11: Selective Jamming
Minimizing Wake Word Mute Rate
  Avoid disturbing the VAs’ basic functionalities
Maximizing Private Speech Mute Rate
  Ensure the private speech is successfully obfuscated by the jamming signal
Whether 90% Private Speech Mute Rate and 1% Wake Word Mute Rate is enough for MicShield?

## Slide 12: Selective Jamming
Use end-to-end evaluation metrics to balance the trade-off
  Wake Word Misdetection  First priority
  Private Speech Word Recognition Rate Phoneme-level leakage is negligible
Achieves 5% Wake word Misdetection Rate (the same as w/o MicShield),
while 0.03% Private Speech Word Recognition Rate (e.g, “I”, “a”, “am”, “as”).

## Slide 13: Challenges
How to enable the effective & practical jamming?
  Jamming a single microphone
  Jamming a microphone array

## Slide 14: Adversaries Attack Capabilities
Access the always-on microphones recordings;
Post processing algorithm to enhance the sound quality
  Microphone-array based speech enhancement methods
Infer the semantic content
  Use existing ASR algorithms
  Use human perception
Worst case protection scenario:
High Sound Pressure Level (SPL) private speech
Advanced VAs with microphone arrays

## Slide 15: Inaudible Jamming
[1] Inaudible voice commands: The long-range attack and defense. NSDI 2018
To prevent disturbing users, we reuse the inaudible jamming methods based on the literature.

## Slide 16: Jamming a single microphone
Inaudible Jamming Sound to avoid disturbing users
(Refer to inaudible voice attack by using ultrasound)
Frequency distortion jamming
Frequency distortion jamming can effectively protect the speech privacy for the single-microphone VA when the speech SNR is less than −15 dB.

## Slide 17: Jamming a microphone array
Challenge: How to jam these microphone arrays?
Beamforming based Attack：
The 6-microphone beamforming to circumvent MicShield protection can enhance the speech SNR by 12 dB.
Beamforming based Attack
Beamforming-based Attack

## Slide 18: Jamming a microphone array
Gain Suppression Jamming
  Transmit high-volume sound to saturate the microphone
  Traditionally, the volume needs 110 dBA to enable gain suppression jamming
  New Challenge: How to make all the microphones saturate?
Gain suppression jamming: (a) zoomed-in saturated jammed signal in time domain; (b) spectrogram of jammed signal.
Beamforming-based Attack

## Slide 19: Jamming a microphone array
Jamming noise volume V.S. audibility and safety
  High input power will trigger the speaker non-linearity and make the sound audible.
  High volume ultrasound is not safe for users
Jamming noise volume V.S. coverage
The largest jamming coverage for a single ultrasonic transducer even with a class-D amplifier.
More powerful amplifier may make the jamming sound audible.

## Slide 20: Jamming a microphone array
Proposed methods:
  Design an Acoustic Waveguide Design to extend the coverage
  “Acoustic multiplexer”
  20 cm flexible silicone tube will also enable the gain suppression jamming.
  3D model for MicShield
  Jamming microphone array w/ shield

## Slide 21: Implementation

## Slide 22: Generalization
Generalizations across Wake Words
  “Alexa”, “Amazon”, “Computer”, “Echo”
Generalizations for multiple wake words at the same time.
  “OK Google”, “Hey Google”
  Fine-tune the phoneme recognition model for multiple wake words.
Generalizations across VA Devices
  Amazon Echo Dot (4 microphones)
  Google Home Mini (2 microphones)

## Slide 23: Conclusion
Automatically protect speech privacy against always-on microphones
Introduces a novel selectively jamming mechanism, which can obfuscate private speech while passing the voice command.
Prototype implementation and experiments verify the feasibility and effectiveness.
Project Alias, 2019

## Slide 24
Thank you
Q&A